## Slide 1
We discover the mechanisms that drive environmental change.
We conduct interdisciplinary science that can help us understand and manage grand challenges surrounding climate change, water, agriculture, and ecosystems health.
instaar.colorado.edu
@instaar

## Slide 2: Overview
Intro to hydrology
  Hydrologic cycle
  Continuity equation
  Hydrologic equation
Measuring snow
Hydrograph
Mountains as water towers
Snow/ice melt models
Climate change

## Slide 4: Water fluxes

## Slide 6
GLOBAL WATER USERS

## Slide 7
INCREASING GLOBAL USE OF WATER

## Slide 8: Hydrologic cycle components
Each path of hydrologic cycle involves one or more of the following (a) transportation of water (b) temporary storage and (c) change of phase/state.
The quantities of water going through various individual paths of the hydrologic cycle can be described by the continuity equation or hydrologic equation.

## Slide 9: Conservation of mass
The principle of conservation of mass states
simply that mass must be conserved for any
fluid in motion.
The total water resources of the earth are
constant.
Which leads to the concept of a control
volume.

## Slide 10: Continuity equation
q = i – ΔS
  i is the rate of input (e.g. of precipitation)
  q is the rate of output (e.g. of runoff) and
  dS/dt is the rate of change in storage (e.g. of a lake)
For example, the basis of reservoir management to control in-stream flows (q) below the reservoir.

## Slide 11: Residence Time (Tr)
the average duration for a water molecule to pass through a subsystem of the hydrologic cycle
Tr = Volume of water in storage (S) in a subsystem / Flow rate (Q) in the same subsystem.
Tr = S/Q

## Slide 12: Residence times
Oceans about 3,000 years
Glacier ice 20-100 years
  900,000 years oldest ice in Antarctica
Atmosphere about 7-9 days
Humans about 4 days

## Slide 13: Hydrologic equation
Mass inflow – mass outflow = change in storage
P – R – G – E – T = S
where P – precipitation, primary input and the starting point in the analysis; R – runoff; G – groundwater; E – evaporation; T – transpiration. All terms in equation have dimensions of volume but can be expressed as depth over the catchment. Infiltration does not appear explicitly in the water budget equation, because it is loss to runoff but a gain to groundwater system.

## Slide 14: Hydrologic equation
If Gin = Gout, we can rewrite as
Q = P – ET ±ΔS, and if ΔS = 0, then
Q = P – ET, and
ET = P – Q, and
Q/P is runoff ratio, the fraction of precip that is converted to discharge
  0.20 for Africa
  0.44 for Europe

## Slide 15
HYDROLOGIC EQUATION
Q = P – ET +- DS
Q is discharge
P is precipitation
ET is evapotranspiration
S is storage (usually groundwater)

## Slide 16: Storage term: Snow
Snow and glacier ice are part of the storage term in the hydrologic equation
Snow is a renewable resource, and generally not carried over from one year to the next.
However, in big years, it can be. In those years, it’s a negative storage term

## Slide 17: Storage term: Glaciers
Glacier ice is fossil (old) water in storage.
Some glacier ice melts every year. That’s normal.
In general, the melted glacial ice is replaced with new snow high in the basin. There is no change in the storage term.
If there is drought, or a low snow year, there will be more ice melt than replaced by snow, and we have a positive storage term.

## Slide 18: Measuring snowfall
Courtesy Gene Rose

## Slide 19
5% increase

## Slide 20: Standard rain gauge

## Slide 21: Undercatch of snow by precip gauges
Adam and Lettenmaier, 2002

## Slide 22: More snow than the gauge can handle
Niwot Ridge; 1995 snow storm
Wet, heavy snowfall where
accumulation was deeper than
the gauge was high

## Slide 23: Br
Bridging at orifice leads to undercatch

## Slide 24: Snowpits
Most accurate measurement of snow depth, density, and SWE.
Obviously time-consuming.

## Slide 25
Snow density: Sipre sampler

## Slide 26
Snow density: Kelly cutter

## Slide 27: Snow Courses

## Slide 28: Federal or Mt. Rose snow sampler.

## Slide 29: Federal sampler in action

## Slide 30: SnoTel Site
Measures only SWE
-no density
-no depth
Manometer measures
pressure
Manual calibration
with Mt Rose
sampler

## Slide 31: Enhanced SnoTel Site

## Slide 32: Meteor Burst telemetry

## Slide 34: LIDAR
LIDAR (Light Detection and Ranging) is an optical remote sensing technology that measures properties of scattered light to find range and/or other information of a distant target.
The prevalent method to determine distance to an object or surface is to use laser pulses.

## Slide 35
Accuracy 10-20 cms in all three directions

## Slide 36: NWT LIDAR snow depth

## Slide 37: GPS
Use the backscatter from a GPS antenna to measure changes in snow depth over time
Larson et al. 2009 example
Gutmann et al. 2011 example

## Slide 39
Snow depth derived from GPS (red squares), the three SR50 sonic snow depth sensors
(blue lines) and field measurements (black diamonds). Bars on field observations are one
standard deviation. GPS snow depth estimates during the first storm (day of year 85.5-86.5) are
not shown (gray region) because the SNR data indicate that snow was on top of the antenna
Larson et al. 2009.

## Slide 40: GPS home site
http://xenon.colorado.edu/portal

## Slide 41: Stream flow
Stream flow is a fundamental property that affects channel shape and the diversity of stream habitats, the flux of nutrients and pollutants, and the frequency and severity of floods.
Stream flow is controlled by such watershed variables as size, topography, geology, land use and presence of wetlands, as well as climatic variables such as rainfall, snow cover and temperature.

## Slide 42: Unit hydrograph
http://www.bbc.co.uk/bitesize/higher/geography/physical/hydrosphere/revision/1/

## Slide 43: Hortonian overland flow

## Slide 46: Snowmelt delivers water when we need it in the spring and summer
Isotopes show that groundwater
Much more important than previously thought

## Slide 47: Mountains as Water Towers

## Slide 48
Image courtesy of NCAR

## Slide 49
Alpine
4000 m
85% snow
Sub-alpine
3400 m
Montane
2900 m
59% snow
Foothills
2600 m
Plains
1500 m
CLIMATE
&
ECOLOGICAL
ZONES
Image courtesy of NCAR
Notes: Ecological gradient across elevation
Gradient in precipitation amount (highest in the alpine) and proportion of snow (highest in the alpine)
Less known about lower elevations – i.e., montane which is at snowline. Snowline might shift in response to climate change.
49

## Slide 50: Water balance, Como Creek,

## Slide 51: Precipitation increases with elevation

## Slide 54
Image courtesy of NCAR

## Slide 55
Alpine
4000 m
85% snow
Sub-alpine
3400 m
Montane
2900 m
59% snow
Foothills
2600 m
Plains
1500 m
CLIMATE
&
ECOLOGICAL
ZONES
Image courtesy of NCAR
Notes: Ecological gradient across elevation
Gradient in precipitation amount (highest in the alpine) and proportion of snow (highest in the alpine)
Less known about lower elevations – i.e., montane which is at snowline. Snowline might shift in response to climate change.
55

## Slide 56: Specific discharge elevation gradient
Williams et al., 2011

## Slide 57
Como Creek
Runoff
Efficiency
%
87.7
20.0
37.7
12.2
Subsurface
Reservoir
(m3).
109,463
2,430
152
60
Subsurface reservoir storage
Notes: Reservoir in Alpine huge – high permeability and transmissivity in the talus slopes and fractured bedrock
Lower in montane maybe because it does not get filled without a sufficient snowmelt pulse or it is just not present
Subsurface sp discharge: Bet N/A, GG 179 mm, Como 85 mm, GL4 772 mm